STREAM SYSTEMS

Concord, CA (925) 672-7443

HOT*SHOT  INSTRUCTIONS

STEEL

(Green - Steel Shot/Tungsten-Iron/Hevi-shot

(Yellow - See Helpful hints below)

BISMUTH			  (Yellow - Bismuth)

TP/TM  			 (Green  - Reference Point/Tungsten Polymer/Matrix

HOT*SHOT

(If it’s RED – Check for Lead!)

LOW POWER        LEAD

STREAM SYSTEMS

Concord, CA    (925)672-7443

www.streamsystems.com

(Approximate size 4”x 2.5”x 1.5”)

INSTRUCTIONS: As simple as 1,2,3!

1. Momentarily press the rocker switch on the side of the unit until the Green LED (reference point) 	lights. Continue to hold for a second (or click twice) then release.

2. While the Green LED light is lit, place the crimped end of the shell slowly into the unit. The LED 	lights will head in the direction of the material in the shell.   After removing the shell, the LED 	should return back to the Green reference point.

3. The unit will shut off automatically after 20-30 seconds. For more time press the switch again.

Helpful hints in using this device.

As you insert the shell, the LED lights should move in one smooth direction. Solid Steel shells and “common size” Copper Coated Steel should read all the way to the Green LED Light. Large Copper Coated Steel Shot (BBB - T-Shot) may not read all the way to the Green Steel LED, and will end up in the Yellow, depending on the amount of copper coating. With Steel shot that is topped off with Lead, the LEDs will move towards Steel then turn around and may end up in the Yellow. If the LED lights turn around or any Red LED lights come on, the shell should be opened and inspected for LEAD.

Material				Magnetic		Charateristicts

LEAD					NO			SOFT - will squash with plyers

STEEL				YES			VERY HARD - cannot squash

Bismuth				NO			Very Brittle - crumbles if squashed

Tungsten-Iron			SLIGHT		Very Hard

Tungsten-Polymer/Matrix		NO			Soft